## Slide 1: Science
Topic: Good scientific and clinical practice
Route: Health & Science
Lesson 2: Use of equipment
Notes: Image © Shutterstock/Gorodenkoff

## Slide 2: In this lesson, we will:
Explain why it is important to calibrate and test equipment so it is fit for use.
Describe the potential impacts of not maintaining, cleaning and servicing equipment.
Outline how to escalate concerns over faulty or unsuitable equipment.
Introduction
Lesson 3: Use of equipment
Skills:
CS3.2: Working with others
CS6: Communication
CS7.1 Evaluate the project’s processes and outcomes
General competencies:
English:
GEC5 Synthesise information
GEC6 Take part in/lead discussions
Maths:
GMC1 Measuring with precision
GMC2 Estimating, calculating and error spotting

## Slide 3: Look at the image
What different things do scientists measure in the world around us?
Introduction
Lesson 3: Use of equipment
Notes: Image © Unsplash/Pedro Ramos

## Slide 4: Look at the image
Which measurements did you think of?
What else did you come up with?
What measurements are critically important?
Introduction
Lesson 3: Use of equipment
Temperature & humidity
Number of cars per hour
Number of office workers
% transparency
Building material strength
Height of pole
Light intensity
Speed
Mass of bus
Mobile speed data
Heart rate
Steps taken
Blood pressure
Notes: Image © Unsplash/Pedro Ramos

## Slide 5: Why is it important to regularly test equipment?
You will be given some pieces of equipment to take a range of measurements. Your teacher will tell you which measurements to take.
Once all groups have collected their data, compare your readings.
  Which group(s) had the correct readings? How do you know?
  Which piece(s) of equipment is/are faulty? How do you know?
  Why is it important to regularly test equipment to check it is not faulty?
Resources needed
A range of equipment
Lesson 3: Use of equipment
Activity 1

## Slide 6: Why is it important to regularly test equipment?
Regularly testing equipment:
ensures the accuracy of measurements
prolongs the life of equipment
is often required to meet legal requirements.
Lesson 3: Use of equipment
Activity 1
Notes: Image © Shutterstock/Roman Zaiets

## Slide 7: Calibrating equipment
Calibrating weighing scales
Why might laboratory scales need calibrating in a scientific workplace?
Is it sufficient just to set the zero reading?
Is a single calibration mass enough to calibrate laboratory scales?
Lesson 3: Use of equipment
Activity 2
Notes: Image © Shutterstock/LightField Studios

## Slide 8: Why is it important to regularly test equipment?
Follow the steps provided on your worksheet to calibrate a micropipette.
Resources needed
L3 Activity 2 Worksheet
P1000 micropipette
Pipette tips
Distilled water
A beaker
Digital thermometer or temperature probe
Digital balance, resolution ±0.0001g
Balance draught shield
Weighing boats
Lesson 3: Use of equipment
Activity 2
Notes: Image © Shutterstock/stciel

## Slide 9: Calibrating equipment
Calibration ensures that a scientific process or piece of equipment will produce accurate results every time.
Over time, instruments can 'drift' due to normal wear and tear, resulting in inaccurate results. Therefore, it is important that pieces of equipment are properly calibrated before use.
Calibration involves comparing measurement values obtained by a piece of equipment under test, with those of known accuracy. (If found to be incorrect the piece of equipment is then adjusted.)
Activity 2
Lesson 3: Use of equipment
Notes: Image © Shutterstock/Markus Thoenen

## Slide 10: Calibrating equipment
Activity 2
Lesson 3: Use of equipment
As well as ensuring an instrument provides an accurate reading, calibration extends the life of a piece of equipment.
The calibration lifecycle of a piece of equipment varies by instrument. It is also determined by manufacturers’ recommendations, usage and environment of the instrument.
It is a legal requirement to calibrate some instruments, for example, gas detectors. This is to ensure safety standards are met.
Notes: Image © Shutterstock/petroleum man

## Slide 11: Identifying mistakes
For each scenario (1–4), read how a student made a measurement.
Decide where they went wrong.
Repeat the procedure correctly using the equipment supplied.
Bunsen burner
Gauze
Tripod
Mat
Safety glasses
Pipette/syringe
Lesson 3: Use of equipment
Activity 3
Resources needed
Cards cut from L3 Activity 3 Worksheet
Balance
4 x 50cm3 beakers
Salt
Measuring cylinder
Water
Thermometer

## Slide 12: Identifying mistakes – correct procedures
Scenario 1 – Place the empty beaker on the balance, press tare, then remeasure the mass of the beaker with the salt added.
Scenario 2 – Place the measuring cylinder on a table whilst filling the cylinder and reading the volume. To determine the correct volume of liquid, line up the eye to the level of where the liquid sits on the scale before taking the reading. (This avoids parallax error.)
Scenario 3 – The thermometer should be held in the liquid away from the beaker sides when measuring the temperature. The liquid should be stirred before a measurement is taken.
Scenario 4 – Use a pipette/syringe to accurately measure out the volume of liquid and transfer to the beaker. Beakers are not suitable for accurate volume measurements due to their larger graduations.
Lesson 3: Use of equipment
Activity 3
Notes: Image © Shutterstock/BalanceFormCreative

## Slide 13: Escalating concerns
When on placement, a trainee nurse had concerns that a fridge, which was being used to store drugs, was not registering the correct temperature. The fridge temperature display showed fluctuations, even when the door had been closed for a period of time.
Discuss with a partner which of the following steps the student should take:
Switch the appliance off at the wall, wait for five minutes, and switch on again. Check the fridge display resets correctly.
Remove all the drugs from the fridge and store in an alternative fridge.
Place a note on the equipment stating that it is faulty and cannot be used and complete a report form.
Tell a more senior member of staff about the issue.
Lesson 3: Use of equipment
Activity 4

## Slide 14: Escalating concerns
If a piece of equipment is unsuitable for intended use, due to a fault or not being correctly calibrated, you should:
  not use the piece of equipment
  label the piece of equipment as unfit for use
  tell your supervisor/line manager
  fill in any organisational documentation if required.
Lesson 3: Use of equipment
Activity 4

## Slide 15: Plenary
Write down three reasons why it is important to calibrate equipment.
Lesson 3: Use of equipment
Plenary

## Slide 16: In this lesson, we have:
Explained why it is important to calibrate and test equipment so it is fit for use.
Described the potential impacts of not maintaining, cleaning and servicing equipment.
Outlined how to escalate concerns over faulty or unsuitable equipment.
Skills:
CS3.2: Working with others
CS6: Communication
CS7.1 Evaluate the project’s processes and outcomes
General competencies:
English:
GEC5 Synthesise information
GEC6 Take part in/lead discussions
Maths:
GMC1 Measuring with precision
GMC2 Estimating, calculating and error spotting
Lesson 3: Use of equipment
Plenary

## Slide 17: Consolidation
Make a video of either correct, or subtly incorrect, procedures to show to the rest of the group in a later session.
Look at online animations to help develop practical skills you lack confidence in, for example, how to make a solution. Suitable examples can be found here: www.labxchange.org/library
Join in with a measurement challenge courtesy of the National Physical Laboratory (NPL), using your measurement skills: www.npl.co.uk/measurement-at-home
Consolidation
Lesson 3: Use of equipment
Notes: www.labxchange.org/library
www.npl.co.uk/measurement-at-home (with permission)